A New Precise Measurement of
the W Boson Mass at CDF
Ashutosh Kotwal
Duke University
For the CDF Collaboration
University of Wisconsin, Madison
6 November 2012

---
Spontaneous Symmetry Breaking
- 2008 Nobel Prize in Physics
  "for the discovery of the mechanism of spontaneously broken symmetry in subatomic physics"
- The mass of the W boson is linked to the mechanism of Electroweak Symmetry Breaking
Yoichiro Nambu

---
Motivation for Precision Measurements
- The electroweak gauge sector of the standard model, defined by (g, g', v), is constrained by three precisely known parameters
  - αEM (MZ) = 1 / 127.918(18)
  - GF = 1.16637 (1) x 10-5 GeV-2
  - MZ = 91.1876 (21) GeV
- At tree-level, these parameters are related to other electroweak observables, e.g. MW
  - MW2 = παEM / √2GF sin2ϑW
    - where ϑW is the Weinberg mixing angle, defined by
      cos ϑW = MW/MZ

---
Motivation for Precision Measurements
Radiative corrections due to heavy quark and Higgs loops and exotica
Motivate the introduction of the ρ parameter: MW2 = ρ [MW(tree)]2
with the predictions Δρ = (ρ-1) ~ Mtop2 and Δρ ~ ln MH
In conjunction with Mtop, the W boson mass constrains the mass of the Higgs boson, and possibly new particles beyond the standard model

---
Detecting New Physics through Precision Measurements
- Willis Lamb (Nobel Prize 1955) measured the difference between energies of 2S½ and 2P½ states of hydrogen atom
  - 4 micro electron volts difference compared to few electron volts binding energy
  - States should be degenerate in energy according to tree-level calculation
- Harbinger of vacuum fluctuations to be calculated by Feynman diagrams containing quantum loops
  - Modern quantum field theory of electrodynamics followed ( Nobel Prize 1965 for Schwinger, Feynman, Tomonaga)

---
Contributions from Supersymmetric Particles
- Radiative correction depends on chiral structure of SUSY sector and mass splitting (Δm2) between squarks in SU(2) doublet
- After folding in limits on SUSY particles from direct searches, SUSY loops can contribute ~100 MeV to MW

---
Uncertainty from αEM(MZ)
(40% C.L.)
Line thickness due to δαEM
- δαEM dominated by uncertainty from non-perturbative contributions: hadronic loops in photon propagator at low Q2
- equivalent δMW ≈ 4 MeV for the same Higgs mass constraint
  - Was equivalent δMW ≈ 15 MeV a decade ago

---
Progress on Mtop at the Tevatron
- From the Tevatron, ΔMtop = 0.9 GeV => ΔMH / MH = 8%
- equivalent ΔMW = 6 MeV for the same Higgs mass constraint (and further improvements possible from Tevatron and LHC)
- 2011 world average ΔMW = 23 MeV
  - progress on ΔMW has the biggest impact on Higgs constraint

---
Motivation II
- SM Higgs fit: MH = 94+29-24 GeV (LEPEWWG)
- Direct searches: MH ~ 125 GeV (ATLAS, CMS)
In addition to the Higgs,
is there another missing piece ?
AFBb vs ALR: ~3σ
Must continue improving
precision of MW , Mtop ...
other precision measurements
constrain Higgs, equivalent
 to δMW ~ 15 MeV
Motivate direct measurement of MW at the 15 MeV level and better

---
Motivation III
- Generic parameterization of new physics contributing to W and Z boson self-energies through radiative corrections in propagators
  - S, T, U parameters (Peskin & Takeuchi, Marciano & Rosner, Kennedy & Langacker, Kennedy & Lynn)
ΠWW(q2)
ΠV V
S+U ~ slope
ΠZZ (q2)
S ~ slope
T
q2

---
Motivation III
- Generic parameterization of new physics contributing to W and Z boson self-energies: S, T, U parameters (Peskin & Takeuchi)
Additionally, MW is the
only measurement which
constrains U
MH ~ 120 GeV
MH > 600 GeV
(from P. Langacker, 2012)
 MW and Asymmetries are the most powerful observables in this parameterization

---
1998 Status of MW vs Mtop

---
2012 Status of MW vs Mtop

---
Previous CDF Result (200 pb-1)
Transverse Mass Fit Uncertainties (MeV)
(CDF, PRL 99:151801, 2007; Phys. Rev. D 77:112001, 2008)
Total uncertainty of 48 MeV on W mass
Systematic uncertainties shown in green: statistics-limited by control data samples

---
W Boson Production at the Tevatron
Quark
Gluons
Lepton
W
Antiquark
Quark-antiquark annihilation
dominates (80%)
Lepton pT carries most of W mass
information, can be measured precisely (achieved 0.01%)
Initial state QCD radiation is O(10 GeV), measure as soft 'hadronic recoil' in
calorimeter (calibrated to ~0.5%)
dilutes W mass information, fortunately pT(W) << MW
Neutrino

---
W Boson Production at the Tevatron
Quark
Gluons
Lepton
W
Antiquark
e
Quark-antiquark annihilation
dominates (80%)
Lepton pT carries most of W mass
information, can be measured precisely (achieved 0.01%)
Initial state QCD radiation is O(10 GeV), measure as soft 'hadronic recoil' in
calorimeter (calibrated to ~0.5%)
dilutes W mass information, fortunately pT(W) << MW
Neutrino

---
 Quadrant of Collider Detector at Fermilab (CDF)
Central hadronic calorimeter
EM calorimeter
provides precise
electron energy
measurement
Central electromagnetic calorimeter
.η = 1
COT provides
precise lepton track momentum
measurement
Calorimeters measure
hadronic recoil particles
Select W and Z bosons with central ( | η | < 1 ) leptons

---
 Collider Detector at Fermilab (CDF)
Muon
detector
Central
hadronic
calorimeter
Central
outer
tracker
(COT)

---
Event Selection
- Goal: Select events with high pT leptons and small hadronic recoil activity
  - to maximize W mass information content and minimize backgrounds
- Inclusive lepton triggers: loose lepton track and muon stub / calorimeter cluster requirements, with lepton pT > 18 GeV
  - Kinematic efficiency of trigger ~100% for offline selection
- Offline selection requirements:
  - Electron cluster ET > 30 GeV, track pT > 18 GeV
  - Muon track pT > 30 GeV
  - Loose identification requirements to minimize selection bias
- W boson event selection: one selected lepton, |u| < 15 GeV & pT(ν) > 30 GeV
  - Z boson event selection: two selected leptons

---
W & Z Data Samples
- Integrated Luminosity (collected between February 2002 – August 2007):
  - Electron and muon channels: L = 2.2 fb-1
  - Identical running conditions for both channels, guarantees cross-calibration
- Event selection gives fairly clean samples
  - Mis-identification backgrounds ~ 0.5%

---
Analysis Strategy

---
 Strategy
Maximize the number of internal constraints and cross-checks
Driven by two goals:
1) Robustness: constrain the same parameters in as many different ways as possible
2) Precision: combine independent measurements after showing consistency

---
Outline of Analysis
Energy scale measurements drive the W mass measurement
- Tracker Calibration
  - alignment of the COT (~2400 cells) using cosmic rays
  - COT momentum scale and tracker non-linearity constrained using J/ψ μμ and ϒ μμ mass fits
  - Confirmed using Z μμ mass fit
- EM Calorimeter Calibration
  - COT momentum scale transferred to EM calorimeter using a fit to the peak of the E/p spectrum, around E/p ~ 1
  - Calorimeter energy scale confirmed using Z ee mass fit
- Tracker and EM Calorimeter resolutions
- Hadronic recoil modelling
  - Characterized using pT-balance in Z ll events

---
Drift Chamber (COT) Alignment
COT endplate
geometry

---
Internal Alignment of COT
Use a clean sample of ~400k cosmic rays for cell-by-cell internal alignment
- Fit COT hits on both sides simultaneously to a single helix (A. Kotwal, H. Gerberich and C. Hays, NIM A506, 110 (2003))
  - Time of incidence is a floated parameter in this 'dicosmic fit'

---
Residuals of COT cells after alignment
CDFII preliminary
Before alignment
Cell number (φ)
after alignment
25
-25
Cell number (φ)
Final relative alignment of cells ~2 μm (initial alignment ~50 μm)
Residual (microns)

---
Cross-check of COT alignment
- Cosmic ray alignment removes most deformation degrees of freedom, but “weakly constrained modes” remain
- Final cross-check and correction to beam-constrained track curvature based on difference of <E/p> for positrons vs electrons
- Smooth ad-hoc curvature corrections as a function of polar and azimuthal angle: statistical errors => ΔMW = 2 MeV
CDFII preliminary L = 2.2 fb-1

---
Signal Simulation and Fitting

---
Signal Simulation and Template Fitting
- All signals simulated using a Custom Monte Carlo
  - Generate finely-spaced templates as a function of the fit variable
  - perform binned maximum-likelihood fits to the data
- Custom fast Monte Carlo makes smooth, high statistics templates
  - And provides analysis control over key components of the simulation
MW = 81 GeV
Monte Carlo template
MW = 80 GeV
We will extract the W mass from six kinematic distributions: Transverse mass, charged lepton pT and missing ET using both electron and muon channels

---
Generator-level Signal Simulation
PHOTOS
RESBOS
- Generator-level input for W & Z simulation provided by RESBOS (C. Balazs & C.-P. Yuan, PRD56, 5558 (1997) and references therein), which
  - Calculates triple-differential production cross section, and pT-dependent double-differential decay angular distribution
  - calculates boson pT spectrum reliably over the relevant pT range: includes tunable parameters in the non-perturbative regime at low pT
- Multiple radiative photons generated according to PHOTOS (P. Golonka and Z. Was, Eur. J. Phys. C 45, 97 (2006) and references therein)

---
Validation of QED Calculations
- Extensive comparisons between PHOTOS and HORACE (C.M. Carloni Calame, G. Montagna, O. Nicrosini and A. Vicini, JHEP 0710:109,2007) programs
  - Comparing multi-photon final state radiation algorithms
  - Including multi-photon radiation from all charged lines (HORACE), and consistency with exact one-photon calculation
Validations confirm systematic uncertainty due to QED radiation of 4 MeV
PHOTOS
HORACE

---
Uncertainties in QED Calculations
- Extensive studies performed on uncertainties arising from
  - leading logarithm approximation
  - Multi-photon calculation
  - higher order soft and virtual corrections
  - Electron-positron pair creation (included at LO)
  - QED/QCD interference
  - dependence on electroweak parameters/scheme
- Total systematic uncertainty due to QED radiation of 4 MeV on W mass

---
Constraining Boson pT Spectrum
Fit the non-perturbative parameter g2 and QCD coupling αS in RESBOS to pT(ll) spectra:
ΔMW = 5 MeV
Position of peak in boson pT spectrum
 depends on g2
Tail to peak ratio depends on αS
Data
Data
Data
Data
Simulation
Simulation
Simulation
Simulation

---
Outline of Analysis
Energy scale measurements drive the W mass measurement
- Tracker Calibration
  - alignment of the COT (~2400 cells) using cosmic rays
  - COT momentum scale and tracker non-linearity constrained using J/ψ μμ and ϒ μμ mass fits
  - Confirmed using Z μμ mass fit
- EM Calorimeter Calibration
  - COT momentum scale transferred to EM calorimeter using a fit to the peak of the E/p spectrum, around E/p ~ 1
  - Calorimeter energy scale confirmed using Z ee mass fit
- Tracker and EM Calorimeter resolutions
- Hadronic recoil modelling
  - Characterized using pT-balance in Z ll events

---
Custom Monte Carlo Detector Simulation
- A complete detector simulation of all quantities measured in the data
- First-principles simulation of tracking
  - Tracks and photons propagated through a high-resolution 3-D lookup table of material properties for silicon detector and COT
  - At each material interaction, calculate
    - Ionization energy loss according to detailed formulae and Landau distribution
    - Generate bremsstrahlung photons down to 0.4 MeV, using detailed cross section and spectrum calculations
    - Simulate photon conversion and compton scattering
    - Propagate bremsstrahlung photons and conversion electrons
    - Simulate multiple Coulomb scattering, including non-Gaussian tail
  - Deposit and smear hits on COT wires, perform full helix fit including optional beam-constraint

---
Custom Monte Carlo Detector Simulation
- A complete detector simulation of all quantities measured in the data
- First-principles simulation of tracking
  - Tracks and photons propagated through a high-resolution 3-D lookup table of material properties for silicon detector and COT
  - At each material interaction, calculate
    - Ionization energy loss according to complete Bethe-Bloch formula
    - Generate bremsstrahlung photons down to 4 MeV, using detailed cross section and spectrum calculations
    - Simulate photon conversion and compton scattering
    - Propagate bremsstrahlung photons and conversion electrons
    - Simulate multiple Coulomb scattering, including non-Gaussian tail
  - Deposit and smear hits on COT wires, perform full helix fit including optional beam-constraint
e+
e-

e-
e-
Calorimeter

---
3-D Material Map in Simulation
Built from detailed construction-level knowledge of inner tracker: silicon ladders, bulkheads, port-cards etc.
- Tuned based on studies of inclusive photon conversions
- Radiation lengths vs (φ,z) at different radii shows localized nature of material distribution
φ
Z (cm)
Include dependence on type of material via
Landau-Pomeranchuk-Migdal suppression of soft bremsstrahlung

---
Tracking Momentum Scale

---
Tracking Momentum Scale
Set using J/ψ μμ and ϒ μμ resonance and Z μμ masses
  - Extracted by fitting J/ψ mass in bins of 1/pT(μ), and extrapolating momentum scale to zero curvature
  - J/ψ μμ mass independent of pT(μ) after 4% tuning of energy loss
Data
Simulation
 Δp/p
J/ψ μμ
mass fit (bin 5)
Default energy loss * 1.04
<1/pT(μ)> (GeV-1)

---
Tracking Momentum Scale
ϒ μμ resonance provides
  - Momentum scale measurement at higher pT
  - Validation of beam-constaining procedure (upsilons are promptly produced)
  - Cross-check of non-beam-constrained (NBC) and beam-constrained (BC) fits
Data
Simulation
NBC ϒ μμ
mass fit

---
Tracking Momentum Scale Systematics
Systematic uncertainties on momentum scale
ΔMW,Z = 6 MeV
Uncertainty dominated by QED radiative corrections and magnetic field
non-uniformity

---
Tracking Momentum Scale
ϒ μμ resonance provides
  - Cross-check of non-beam-constrained (NBC) and beam-constrained (BC) fits
  - Difference used to set additional systematic uncertainty
Data
Simulation
   BC ϒ μμ
   mass fit

---
Z μμ Mass Cross-check & Combination
- Using the J/ψ and ϒ momentum scale, performed “blinded” measurement of Z mass
  - Z mass consistent with PDG value (91188 MeV) (0.7σ statistical)
  - MZ = 91180 ± 12stat ± 9momentum ± 5QED ± 2alignment MeV
Data
Simulation
M(μμ) (GeV)

---
 Tracker Linearity Cross-check & Combination
- Final calibration using the J/ψ, ϒ and Z bosons for calibration
- Combined momentum scale correction:
  Δp/p = ( -1.29 ± 0.07independent ± 0.05QED ± 0.02align ) x 10 -3
ΔMW = 7 MeV

---
EM Calorimeter Response

---
Calorimeter Simulation for Electrons and Photons
- Distributions of lost energy calculated using detailed GEANT4 simulation of calorimeter
  - Leakage into hadronic
    calorimeter
  - Absorption in the coil
  - Dependence on incident angle
    and ET
- Energy-dependent gain (non-linearity) parameterized and fit from data
- Energy resolution parameterized as fixed sampling term and tunable constant term
  - Constant terms are fit from the width of E/p peak and Z ee mass peak

---
EM Calorimeter Scale
E/p peak from W eυ decays provides measurements of EM calorimeter scale and its (ET-dependent) non-linearity
ΔSE = (9stat ± 5non-linearity ± 5X0 ± 9Tracker) x 10-5
Setting SE to 1 using E/p calibration from combined W eυ and Z ee samples
ΔMW = 13 MeV
Data
Simulation
Tail of E/p spectrum
used for tuning model of
radiative material
ECAL / ptrack

---
Consistency of Radiative Material Model
- Excellent description of E/p spectrum tail
- radiative material tune factor: SX0 = 1.026 ± 0.003stat ± 0.002background achieves consistency with E/p spectrum tail
Data
Simulation
Default energy loss * 1.026
ECAL / ptrack

---
Measurement of EM Calorimeter Non-linearity
- Perform E/p fit-based calibration in bins of electron ET
- GEANT-motivated parameterization of non-linear response:	SE = 1 + β log(ET / 39 GeV)
- Tune on W and Z data: β = (5.2±0.7stat) x 10-3
  => ΔMW = 4 MeV
W data
Z data

---
EM Calorimeter Uniformity
- Checking uniformity of energy scale in bins of electron pseudo-rapidity
W data

---
Z ee Mass Cross-check and Combination
- Performed “blind” measurement of Z mass using E/p-based calibration
  - Consistent with PDG value (91188 MeV) within 1.4σ (statistical)
  - MZ = 91230 ± 30stat ± 10calorimeter ± 8momentum ± 5QED ± 2alignment MeV
- Combine E/p-based calibration with Z ee mass for maximum precision
  - SE = 1.00001 ± 0.00037
ΔMW = 10 MeV
Data
Data
Simulation
Simulation
M(ee) ( GeV)

---
Lepton Resolutions
- Tracking resolution parameterized in the custom simulation by
  - Radius-dependent drift chamber hit resolution σh ~ (150 ± 1stat) μm
  - Beamspot size σb= (35 ± 1stat) μm
  - Tuned on the widths of the Z μμ (beam-constrained) and ϒ μμ (both beam constrained and non-beam constrained) mass peaks
  - . => ΔMW = 1 MeV (muons)
- Electron cluster resolution parameterized in the custom simulation by
  - 12.6% / √ET (sampling term)
  - Primary constant term κ = (0.68 ± 0.05stat) %
  - Secondary photon resolution κγ = (7.4 ± 1.8stat) %
  - Tuned on the widths of the E/p peak and the Z ee peak (selecting radiative electrons) => ΔMW = 4 MeV (electrons)

---
Hadronic Recoil Model

---
Lepton Tower Removal
- We remove the calorimeter towers containing lepton energy from the hadronic recoil calculation
  - Lost underlying event energy is measured in φ-rotated windows
ΔMW = 2 MeV
Muon channel W data
Electron channel W data
 .η
 .η
 .φ
φ

---
Constraining the Hadronic Recoil Model
Exploit similarity in production
and decay of W and Z bosons
Detector response model for
hadronic recoil tuned using
pT-balance in Z ll events
Transverse momentum of Hadronic recoil (u) calculated as 2-vector-sum over calorimeter towers

---
Hadronic Recoil Simulation
Recoil momentum 2-vector u has
- a soft 'spectator interaction' component, randomly oriented
  - Modelled using minimum-bias data with tunable magnitude
- A hard 'jet' component, directed opposite the boson pT
  - PT-dependent response and resolution parameterizations
  - Hadronic response R = ureconstructed / utrue parameterized as a logarithmically increasing function of boson pT motivated by Z boson data
Data
Simulation

---
Tuning Recoil Response Model with Z events
Project the vector sum of pT(ll) and u on a set of orthogonal axes defined
by boson pT
Mean and rms of projections as a function of pT(ll) provide
information on hadronic model parameters
pTZ
μ
μ
u
Hadronic model parameters
tuned by minimizing χ2
between data and simulation
Data
Simulation
ΔMW = 4 MeV
mean of pT-balance (GeV)

---
Tuning Recoil Resolution Model with Z events
At low pT(Z), pT-balance constrains hadronic resolution due to
underlying event
pTZ
μ
μ
u
ΔMW = 4 MeV
Data
Simulation
At high pT(Z), pT-balance constrains jet resolution
Resolution of pT-balance (GeV)

---
Testing Hadronic Recoil Model with W events
u
(recoil)
Compare recoil distributions
 between simulation and data
l
Data
Data
Simulation
Simulation
Recoil projection (GeV) on lepton direction
Recoil projection (GeV) perpendicular to lepton

---
Testing Hadronic Recoil Model with W events
 Recoil model validation
plots confirm the consistency
of the model
Data
Simulation
 pT(W), electron channel
Data
Data
Simulation
Simulation
u
(recoil)
l
 pT(W), muon channel

---
Parton Distribution Functions
- Affect W kinematic lineshapes through acceptance cuts
- We use CTEQ6 as the default PDF
- Use ensemble of 'uncertainty' PDFs
  - Represent variations of eigenvectors in the PDF parameter space
  - compute δMW contribution from each error PDF
- Using MSTW2008 PDF ensemble defined for 68% CL, obtain systematic uncertainty of 10 MeV
- Comparing CTEQ and MSTW at 90% CL, yield similar uncertainty (CTEQ is 10% larger)
  - Cross-check: default MSTW2008 relative to default CTEQ6 yields 6 MeV shift in W mass

---
Backgrounds in the W sample
Backgrounds are small (except Z μμ with a forward muon)

---
W Mass Fits

---
Blind Analysis Technique
- All W and Z mass fit results were blinded with a random [-75,75] MeV offset hidden in the likelihood fitter
- Blinding offset removed after the analysis was declared frozen
- Technique allows to study all aspects of data while keeping Z mass and W mass result unknown within 75 MeV

---
  W Transverse Mass Fit
Muons
Data
Simulation

---
  W Mass Fit using Lepton pT
Electrons
Data
Simulation

---
  Summary of W Mass Fits

---
Combined Results
- Combined electrons (3 fits): MW = 80406 ± 25 MeV, P(χ2) = 49%
- Combined muons (3 fits): MW = 80374 ± 22 MeV, P(χ2) = 12%
- All combined (6 fits): MW = 80387 ± 19 MeV, P(χ2) = 25%

---
Previous CDF Result (200 pb-1)
Transverse Mass Fit Uncertainties (MeV)
Systematic uncertainties shown in green: statistics-limited by control data samples

---
New CDF Result (2.2 fb-1)
Transverse Mass Fit Uncertainties (MeV)
Systematic uncertainties shown in green: statistics-limited by control data samples

---
   Combined W Mass Result, Error Scaling

---
2012 Status of MW vs Mtop

---
W Boson Mass Measurements from Different Experiments
World average
computed by TeVEWWG
ArXiv: 1204.0042
5 fb-1
(PRL 108, 151804)
2.2 fb-1
(PRL 108, 151803)
Previous world
 average
= 80399 ± 23 MeV
new CDF result more precise than other measurements

---
Improvement of MW Uncertainty with Sample Statistics
Run2 (e)
Non-scaling floor (11 MeV) dominated by PDF uncertainty (10 MeV)

---
Future MW Measurements at Tevatron and LHC
- Factor of 2-5 bigger samples of W and Z bosons available
- Huge samples at LHC
- For most of the sources of systematic uncertainties, we have demonstrated that we can find ways to constrain them with data and scale systematic uncertainties with data statistics
- Exception is the PDF uncertainty, where we have not made a dedicated effort to constrain the PDFs within the analysis
- We need to address specific PDF degrees of freedom to answer the question:
  - Can we approach total uncertainty on MW ~ 10 MeV at the Tevatron? 5 MeV at the LHC?
- (A.V. Kotwal and J. Stark, Ann. Rev. Nucl. Part. Sci., vol. 58, Nov 2008)

---
PDF Uncertainties – scope for improvement
- Newer PDF sets, e.g. CT10W include more recent data, such as Tevatron W charge asymmetry data
- Dominant sources of W mass uncertainty are the dvalence and d-u degrees of freedom
  - Understand consistency of data constraining these d.o.f.
  - PDF fitters increase tolerance to accommodate inconsistent datasets
- Fermilab/Seaquest, Tevatron and LHC measurements that can further constrain PDFs:
  - Drell-Yan, Z boson rapidity distribution
  - W → lν lepton rapidity distribution
  - W boson charge asymmetry

---
Summary
- The W boson mass is a very interesting parameter to measure with increasing precision
- New Tevatron W mass results are very precise:
  - MW = 80387 ± 19 MeV (CDF) = 80375 ± 23 MeV (D0) = 80385 ± 15 MeV (world average)
- New global electroweak fit MH = 94+29-24 GeV @ 68% CL (LEPEWWG)
  - SM Higgs prediction is pinned in the low-mass range
  - confront mass of new particle from direct search result ~ 125 GeV
- Looking forward to ΔMW < 10 MeV from full Tevatron dataset goal of ΔMW < 5 MeV from LHC data

---
Z ee Mass Cross-check using Electron Tracks
- Performed “blind” measurement of Z mass using electron tracks
  - Consistent with PDG value within 1.8σ (statistical)
- Checks tracking for electrons vs muons, and model of radiative energy loss
  - SE = 1.00001 ± 0.00037
Data
Simulation
M(ee) ( GeV)

---
  W Transverse Mass Fit
Electrons
Data
Simulation

---
  W Lepton pT Fit
Muons
Data
Simulation

---
  W Missing ET Fit
Electrons
Data
Simulation

---
  W Missing ET Fit
Muons
Data
Simulation

---
  W Mass Fit Residuals, Muon Channel

---
  W Mass Fit Residuals, Electron Channel

---
  W Mass Fit Window Variation, mT Fit

---
  W Mass Fit Window Variation, pT(l) Fit

---
  W Mass Fit Window Variation, pT(υ) Fit

---
  W Mass Fit Results

---
   Combined W Mass Result, Error Scaling

---
  pT(ν) Fit Systematic Uncertainties

---
  Combined Fit Systematic Uncertainties

---
  pT(l) Fit Systematic Uncertainties

---
QCD Background Estimation in Muon Channel

---
Decay-in-Flight Background Estimation in Muon Channel

---
Motivation II
Separate fits for MH using only leptonic and only hadronic measurements of asymmetries: marginal difference in preferred Higgs mass (from M. Chanowitz, February 2007 Seminar, Fermilab)
Possible explanations:
Statistical fluctuation
 Systematic experimental bias
New physics contributions:
      To raise MH prediction of leptonic asymmetries:
Minimal SuperSymmetric Standard Model	Altarelli et. al.
4th family of fermions	Okun et. al.
Opaque branes	Carena et. al.
      New physics in b-quark asymmetry requires large modification to Zbb vertex
other precision measurements
constrain Higgs, equivalent
 to δMW ~ 15 MeV

---
Parameters of Electro-Weak Interactions

---
Radiative Corrections to W Boson Mass

---
Radiative Corrections to Electromagnetic Coupling

---
Systematic Uncertainties in QED Radiative Corrections

---
Consistency check of COT alignment procedure
- Fit separate helices to cosmic ray tracks on each side
- Compare track parameters (eg. Curvature, shown below) of the two tracks: a measure of track parameter bias
CDFII preliminary
False curvature smaller than 0.1% for
40 GeV track, over the length of the COT
Z (cm)
Δ c (cm-1)

---
Previous MW vs Mtop

---
Updated MW vs Mtop

---
 MW vs Mtop